## Slide 1: Developments in WLAN Standards
Jim Zyren
Intersil

## Slide 2: WLAN Standards
IEEE 802.11
  Most successful WLAN standard
  Result of 10 years of development
  Huge increase in popularity over last 24 months
  Focus of today’s discussion
Other standards
  HiperLAN2
    Future is unknown
  HomeRF
    No traction after 3 years

## Slide 3: Focus on 802.11
Developments in the PHY
  Wi-Fi (802.11b)
  802.11a
  802.11g
  XDR
Security
  TKIP
  802.1x
W3LAN
QoS

## Slide 4: Developments in the PHY

## Slide 5: Wi-Fi (a.k.a. 802.11b)
First major success in WLAN arena
  >15 million radios WW now, >30 million by end of ‘02
Standard developed in 1998-1999 by IEEE
WECA est’d in 2000 to certify interoperability
Characteristics
  Operates at 2.4 GHz
  Offers 3 non-overlapping channels
  Supports data rates of 1, 2, 5.5, and 11 Mbps
Single Carrier modulation scheme (CCK):
frequency
Signal Bandwidth
single carrier

## Slide 6: IEEE 802.11a
First products launched in Q4 2001
  More to follow
Developed by IEEE at same time as Wi-Fi
Operates at 5 GHz
  Shorter range
  More channels (8 channels v. 3 for Wi-Fi)
Will be certified for Interoperability by WECA
Much Higher data rates (6, 9,12, 18, 24, 36, 48, 54 Mbps)
Uses Multi-carrier modulation (OFDM):

## Slide 7: 802.11a (cont’d)
Uses Multi-carrier modulation (OFDM)
  Excellent multipath performance
Tsymbol
TFFT
Tguard
TTR
frequency
Signal Bandwidth
multiple
subcarriers
Tsymbol = Symbol Period (4 sec)
TFFT = FFT Period (3.2 sec)
t TR = Transition time (~ 100 nsec?)
Tguard = Guard Interval (~ 700 nsec?)
Frequency Domain Representation
OFDM Time Domain Pulse

## Slide 8: 802.11g
Currently Under Development in IEEE
  Major elements of the standard essentially complete
  Final approval 2H 2002
Provides 54 Mbps data rates @ 2.4 GHz
  Fully backward compatible and interoperable with Wi-Fi
Uses CCK (single carrier) for backward compatibility
Uses OFDM (multicarrier) for higher rates (>11 Mbps)
  802.11 is a listen-before-talk protocol
  “mixed mode” required use of RTS/CTS feature
802.11g offers:
  High data rates (up to 54 Mbps) & Excellent range
  Backward compatibility to Wi-Fi
Key Milestone toward development of “Universal Client”
  Dual band radios

## Slide 9: Mandatory & optional elements of 802.11g
CCK
CCK
OFDM
OFDM
OFDM
CCK
PBCC
CCK
Preamble/Header
Payload
CCK
CCK/OFDM
OFDM
PBCC
optional
mandatory

## Slide 10: 802.11g Packet Exchanges
CCK Packet (11 Mbps)
CCK Ack
OFDM Packet (24 Mbps)
OFDM Ack
CCK RTS
CCK CTS
OFDM Packet (24 Mbps)
OFDM Ack
Conventional CCK Packet Exchange
“Mixed Mode” Packet Exchange
Straight OFDM Packet Exchange

## Slide 11: Throughput Comparison for 802.11g
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
Throuhput
(Mbps)
cck11
pbcc22
ofdm rts/cts
cck-ofdm
ofdm
802.11g Performance (various eements)

## Slide 12: What’s Next?
XDR
  Xtreme Data Rate
    We’ve already used “High Data Rate”
  >100 Mbps
IEEE Study Group possibly formed by mid year
  Entire process for standard development about 2 years
So we gonna do this?
  Will not be trivial
  Several interesting proposals
  Proposals may morph during standards development

## Slide 13: Security

## Slide 14: 802.11i Background
802.11i is an optional extension to the existing 802.11 standard for enhanced security or ESN (Enhanced Security Network)
  Enhanced authentication
  Key management algorithms
  Dynamic session keys
  New Privacy Algorithms
    AES
    TKIP
Intersil will provide full support for 802.11i across all reference designs
Intersil has been a significant contributor to the development of the 802.11i standard
  Significant parts of the standard have been implemented as part of this participation
802.11 MAC
802.1X
Upper Layer Authentication Protocols
Protocol Stackup
Encryption
(WEP, TKIP, AES)
802.11i

## Slide 15: Key Points
Soon to be released replacement for WEP – TKIP
  Very secure
  Developed by significant involvement from cryptographic community
  Current equipment on market is upgradeable
Longer term – even stronger solution - AES
Applies to both Wi-Fi and Wi-Fi5

## Slide 16: Major Elements of 802.11i
TKIP
  WEP replacement from Task Group I
  Based on RC4
  Targeted for legacy equipment
AES based encryption
  Block cipher which replaces WEP and RC4
  Hardware accelerated for optimal performance
    May not be upgradeable in many cases
  Targeted for future Wi-Fi equipment
802.1x

## Slide 17: Temporal Key Integrity Protocol – TKIP
IEEE 802.11 met the week of 1/21/02
  Final elements of TKIP were adopted, final document is now being edited
  AES-based solution development is ongoing
TKIP is the industry response to the weaknesses identified with WEP
  Backward compatible with all or most hardware on the market
  Software upgradeable to existing equipment
  Will defeat any known attacks
  Developed by a respected cryptographic team

## Slide 18: What does TKIP do?
Rapid rekey using 802.1x
  New encryption key generated every 10K packets
  Same protocol as 802.11i AES based solution, but used in different manner
Mixing Function
  IV is cryptographically hashed with the shared key
  Addresses FMS attack
Message Integrity Check (MIC)
  Cryptographic checksum to identify packet alteration
  Addresses Berkley class attacks
IV Sequencing

## Slide 19: Worldwide 802.11a Especially in Europe
Regulations
Tuning Band
DFS & TPC

## Slide 20: European HIPERLAN 2 Background
ETSI BRAN HIPERLAN Type 2 is defined in ETSI TS 101 475
ERC (99)23 Regulations specify spectrum & etiquette
  Dynamic Frequency Selection (DFS)
  Transmit Power Control (TPC)
ETSI EN 301 893 specifies radio conformance tests
  Document now under revision
    Generalizes HL1 & HL2 to “high performance WLAN”
    Clarifies test specifications

## Slide 21: 5GHz European WLAN Rules - Rationale
Rationale
Minimize interference to primary users of the spectrum
  Radio location, radar, earth exploration satellite, etc
2 Techniques
  Spread active radios evenly across allocated spectrum
  (DFS)
    APs determine best frequency for operation based on continuous spectral band activity measurements
    APs and associated STAs can change frequency at any time, to minimize interference in a band
  Manage transmit power (TPC) - don’t overpower
    AP/STA configuration shall operate to reduce the overall transmitted power or interference of the system on other systems in band by 3dB

## Slide 22: 802.11a / HIPERLAN 2 Convergence
IEEE 802.11 created Task Group H to add DFS & TPC and new tuning bands to 802.11a
Task Group formed December 2000
First letter ballot issued October 2001
  Comment resolution underway
Draft standard expected to be stable by September 2001

## Slide 23
Spectrum Allocation at 5 GHz
5.200
5.300
5.400
5.500
5.600
5.700
5.800
5.900
5.100
Europe
USA
Japan
Freq./GHz
5.350
5.150
5.150
5.250
5.350
5.725
5.825
5.150
5.470
5.725
Outdoor 1W EIRP
Indoor 200 mW EIRP
Indoor 200 mW / Outdoor 1 W EIRP
Max mean Tx power
Outdoor 4 W EIRP
Max peak Tx power
DFS & TPC
DFS & TPC
DFS: Dynamic Frequency Selection
TPC: Transmit Power Control

## Slide 24: 5 GHz Spectrum - Europe
HIPERLAN
200 mW
indoor
5.000 5.100 5.200 5.300 5.400 5.500 5.600 5.700 5.800 5.900 6.000 GHz
1. HIPERLAN/2 must comply with (ERC/DEC/(99)23)
2. TPC provides 3dB mitigation factor
HIPERLAN
1 W
indoor/outdoor
ISM
25 mW
5.150 5.350
5.470 5.725
5.725 5.875
Satellite FSS
Aeronautical
Navigation
Radar,
Navigation,
Earth exploration
Satellite
Radio navigation,
Maritime navigation
Radiolocation,
Amateur
3a. DFS across at least 330 MHz (indoor)
3b. DFS across at least
255 MHz (outdoor)
802.11h addressing changes to comply with ERC DFS & TPC requirements
Primary
Users

## Slide 25: Quality of Service

## Slide 26: Overview of 802.11e
What is QoS?
  Provides prioritization and bounded latency fo traffic
  Essential for support of time critical services
    Voice
    Video
    Etc.
802.11e adds a QoS facility to the 802.11 MAC in an upward compatible manner.
Hybrid Coordination Function (HCF) has two channel access mechanisms
  contention-based
  Polled
The two methods can be used separately or together.

## Slide 27: 802.11e
The HCF is mandatory in all QoS Stations and QoS Access Points.
  HCF frame exchanges occur during TXOPs of defined maximum lengths.
  TXOPs may be obtained by the contention-based access mechanism called EDCF (Enhanced Distributed Coordination Function). It provides relative differentiation of traffic based on priority levels.
  TXOPs may be obtained from the Hybrid Coordinator using the polling mechanism.
  The legacy PCF (point coordination function) requires that the polled and contention-based access methods alternate on a fixed, cyclic basis, and limits each poll response to a single frame of unlimited length. The HCF access methods permit both access methods to operate concurrently during the superframe, and limits the time of the response to the granted TXOP. The legacy PCF is an option in the base 802.11 standard, and is also an option for 802.11e, although legacy PCF would never be used in an 802.11e implementation since the HCF is a superset.

## Slide 28: Comparison
Contention-based channel access (EDCF)
  An expansion of the legacy CSMA/CA DCF mechanism to include priorities. The contention window and backoff times are adjusted to change the probability of winning a contention to favor higher priority classes.
  A total of 8 priority levels are available. Only one priority is higher than legacy DCF, and one is equal to legacy.
  Symmetrical and fair – stations and access points use the same mechanism and contend on an equal basis for a given priority.
Hybrid Coordinator Polled Access
  Centrally coordinated access. The Hybrid Coordinator (HC) controls the allocation of time on the medium to stations. The HC has a higher medium access priority than any station.
  The contention-free access mechanisms uses polling. The HC grants a TXOP in a poll.
  Can support traffic streams with specified bandwidth, latency, and jitter, requirements. In conjunction with admission control and bandwidth reservation (RSVP) at higher layers.
  Arbitrary numbers of traffic streams with unique QoS requirements can be supported.

## Slide 29: Structural Diagram
The HCF is the fundamental access mechanism of 802.11e.
  Within the HCF, there are two types of channel access.
  The HCF also provides QoS-specific frame formats, frame exchange sequences, and the concept of Transmit Opportunities (TXOPs), all of which can be used by any of the channel access methods.
Legacy DCF
HCF
Polled
EDCF
Legacy PCF
Legacy DCF
HCF
Legacy PCF
EDCF
The HCF and EDCF are not mutually exclusive options