## Slide 1
Overcome Distance Limitations in
Outdoor Networks
Michael F. Young
President
Young Design Inc.
www.ydi.com
© 2001 Young Design Inc.
Ver: 1.0 Feb 2001
Amplifiers, Converters and Design Considerations

## Slide 2
Purpose of Presentation
To Answer the Questions:
How are long-range license-free radio links achieved?
What does external amp do?
What how is it used and installed?
What improvements do I get?
What about a 2.4/5.8 GHz Converter?

## Slide 3
Long Range Links
What is needed:
Clear Line of Sight
High Gain Antennas
Radio co-located with the Antenna
or
Pole Mounted Amplifiers

## Slide 4
Examples of Radios Co-located with Antennas
Breezecom ODU
with Antenna
YDI EtherAnts and USB Ants
Patents Pending

## Slide 5
Extends the range of 2.4 GHz SS radios by putting the maximum allowable TX power right at the antenna and boosting the RX signals. This has the effect of taking the coax cable loss out of the equation.
Pole Mounted Amplifers

## Slide 6
Radio
AMP
1. TRANSMIT POWER
15 dBm
(32 mW)
3. POWER TO AMP
15 dBm - 5 dB = 10 dBm
(10 mW)
4. POWER TO ANTENNA
10 dBm + 14 dB = 24 dBm
(250 mW)
Gain = 14 dB
Without an external pole mounted amplifier, the power to the antenna would only be 10 dBm (10 mW) !
2. COAX CABLE
TO ANTENNA
Loss = 5 dB
Example Transmit Calculation

## Slide 7
1. RECEIVED SIGNAL
-80 dBm
Gain = 16 dB
2. AMPLIFICATION
-80 dBm + 16 dB = -64 dBm
(Plus amp noise)
3. COAX CABLE TO RADIO
Loss = 5 dB
4. SIGNAL TO RADIO
-64 dBm - 5 dB = - 69 dBm
(Most amp noise lost in cable)
The amp compensates for all the coax cable loss and typically increases the radio’s RX sensitivity a few dB or more.
Example Reception Calculation
Radio
AMP

## Slide 8
For optimum amp performance, the cable loss between it and the antenna must be as low as possible.
In other words: put the amp at the antenna, not at the radio!
An Amplifier "Don't"
Radio
AMP
Long Coax cable
THIS SETUP IS NOT RECOMMENDED!
Antenna

## Slide 9
A simple single channel WIPOP
Wireless
Internet
Point
Of
Presence
Omni-directional Application

## Slide 10
AMP2440 Amp Kit
Pole Mounted Amplifier
Mounting Bracket
DC Power Injector
Installation and User Manual
110-220 VAC Power Supply
Patent Pending

## Slide 11
Free Space Loss
Receiver
Transmitter
Line of Sight
Free Space Loss is:
FSL = 36.6 + 20 log F + 20 log D
Where: F = Freq in MHz
D = Distance in miles
Rule of Thumb: Double/halve the distance -> Add/subtract 6 dB.
FREQ | 36.6+20 log F
2.4 GHz | 104.2
5.8 GHz | 111.8

## Slide 12
System Operating Margin
Client
Transmitter
WIPOP
Receiver
Line of Sight
TX Power
RX Signal
Level
TX Cable
Loss
(e.g., 14dB Sector Antenna)
TX Antenna
RX Antenna
System Operating Margin (SOM) is defined as the difference between the signal needed for good reception (i.e., receiver sensitivity) and the signal level received.
Also referred to as Fade Margin.
Client to WIPOP
(e.g., 24dB Grid Dish)
SOM = RX signal (dBm) - RX sensitivity (dBm) i.e, what you are getting minus what you need

## Slide 13
20 Mile Example: No Amps
Amplifier
Amplifier
Distance = 20 miles
Line of Sight
TX Power
RX Signal
Level
TX Cable
Loss
24 dBi Dish
TX Antenna
RX Antenna
SOM = RX signal (dBm) - RX sensitivity (dBm)
Example: 15 dBm – 5 dB+ 24 dBi – 130 dB + 24 dBi – 5 dB = - 77 dBm RX Signal
- 67 dBm - (- 83 dBm) = 6 dB SOM
24 dBi Dish
(5 dB)
(+15 dBm)
FSL = 130 dB at 2.4 GHz
RX Cable
Loss
(5 dB)

## Slide 14
20 Mile Example With Amps
Amplifier
Amplifier
Distance = 20 miles
Line of Sight
TX Power
RX Signal
Level
TX Cable
Loss
24 dBi Dish
TX Antenna
RX Antenna
SOM = RX signal (dBm) - RX sensitivity (dBm)
Example: 24 dBm + 24 dBi – 120 dB + 24 dBi = - 72 dBm RX Signal
-72 dBm - (- 83 dBm) = 25 dB SOM
24 dBi Dish
(Negligible)
(+24 dBm)
FSL = 130 dB at 2.4 GHz

## Slide 15
When calculating the SOM, do not add the amps RX gain to the SOM equation. Just assume the RX cable loss is zero (or even a small negative number).
SOM Calculation TIP
For SOM calculations, visit:
www.ydi.com/som.php

## Slide 16
Signal to Noise Ratio (SNR)
SNR is the ratio (in dB) between the received signal level and the noise level that the radio is seeing. It is the only thing that determines if a packet of data is successfully demodulated and decoded.
- 90 dBm
- 65 dBm
- 70 dBm
- 75 dBm
- 80 dBm
- 85 dBm
Received
Signal Level
Noise Level
SNR = 15 dB
SNR = - 75 dBm - ( - 90 dBm) = 15 dB
Signal
Levels
- 60 dBm

## Slide 17
In practice, the quality of a radio link is not determined solely by the the SOM calculation. It also includes factors such as the noise floor and interference.
Real Life Systems
Field tests with real equipment and real antennas show that the SNR is typically 3 to 9 dB worse than the calculated SOM, even with no interference.

## Slide 18
Amplifiers cannot be certified. Only systems can be FCC certified.
To ensure FCC compliance, obtain the FCC Grant and the certified system details from your amplifier vendor.
For DSSS radios, make sure that the amp has linear transmitter power amplification and that it does not increase the sideband noise.
2.4 GHz AMP Tips

## Slide 19
WLAN Card Sprectrum
Spectrum of an 802.11b 11Mbps DSSS signal without any amplification.
The first set of sidebands are 40 dB down from the main lobe in the center.
Other sidebands are below the noise floor of the Spectrum Analyzer.

## Slide 20
Amplified with YDI Amp
Spectrum of after amplified by a YDI amplifier.
Its linear power gain results in a clean reproduction of the original signal.

## Slide 21
Amplified with Competitors' Amp
Spectrum of after amplified by a non-linear amplifier.
The amp is in compression. This causes the sidebands to rise and spread noise all over the 2.4 GHz band as well as outside it.
Both amplifiers were driven with a 10 dBm transmit signal at the amp.

## Slide 22
Uses existing low-cost 2.4 GHz SS radios
Converter is pole mounted at the antenna
Like with 2.4 GHz pole mounted amps, coax cable loss is not a factor for both TX and RX signals
2.4/5.8 GHZ Converters
All the TX power is right at the antenna
Can be used in p-p or p-m applications
Patent Pending

## Slide 23
Converts 2.4 SS GHz radios to the 5.8 GHz SS band.
Converter Installation
Directional Antenna
Dish or panel

## Slide 24
CA2458 Kit
Pole Mounted Converter
Mounting Bracket
DC Power Injector
Installation and User Manual
110-220 VAC Power Supply
Patent Pending

## Slide 25
20 Mile Link
Converter
Converter
Distance = 20 miles
Line of Sight
TX Power
RX Signal
Level
TX Cable
Loss
27 dBi Dish
TX Antenna
RX Antenna
SOM = RX signal (dBm) - RX sensitivity (dBm)
Example: 24 dBm – 1 dB + 27 dBi – 138 dB + 27 dBi = - 61 dBm RX Signal
-63 dBm - (-83 dBm) = 22 dB SOM
27 dBi Dish
(1 dB)
(+24 dBm)
FSL = 138 dB at 5.8 GHz

## Slide 26
Q & A Period
Any questions?
Any topics you wish to discuss in more detail?
Comments?

## Slide 27
Thank You
Thank you for your time and attention.
Please visit our website.
www.ydi.com

## Slide 28
Reference Material
These pages have some information that you might find useful……

## Slide 29
Definitions
Difference (or ratio) between two signal levels. Generally used used to describe the effect of system devices on signal strength.
A signal strength level. 0 dBm is defined as 1 mW of power. Small signals are negative numbers. (e.g. - 83 dBm)
The gain of an antenna relative to an isotropic radiator. Used in calculating ERP and range.
NOTE: dB, dBm and dBi are used because systems’ powers, gains and losses can be calculated by simply adding and subtracting.
Effective Radiated Power, equal to the antenna gain added to the power into that antenna. (Technically, called EIRP.)
dBm
ERP
dB
dBi

## Slide 30
Examples of Gain and Loss
Amplification
12dBm
Signal Loss
Gain = 10dB
22dBm
Output Power
Input Power
Coax cable with 7dB loss
(e.g., 100ft LMR400)
Input Power
Output Power
-80 dBm
-73 dBm

## Slide 31
Effective Radiated Power (ERP)
Amplifier
ERP = 24 dBm + 24 dBi
= 48 dBm (64 Watts)
TX Power = + 24dBm
EIRP = Transmitted Antenna gain (dBi) + TX power into it (dBm)
Antenna Gain = 24 dBi
EIRP = Effective Isotropic Radiated Power

## Slide 32
dBm vs. Watts
Rule of Thumb
Double/Half Power
Add/Subtract 3dB
Ten Times/One-tenth power
Add/Subtract 10dB
Power
1 mW
Example: Convert 250 mW to dBm
dBm = 10 log
10 log
250
1 mW
= 10 X 23.97 = 24 dBm

## Slide 33
Sample Hardware For a
Wireless Internet System