## Slide 1
NLOS in the microwave bands
CDMA vs OFDM
Bernard Aboussouan
VP Marketing
Broadband Wireless World Forum
February 12-14, 2002
Anaheim, CA

## Slide 2: Product Evaluation Criteria
Coverage: Link Budget & fade margin not cell radius
  Coverage, availability, height of antennas, building penetration loss
  Propagation model: Cost 231, Erceg B/ C, Tree canopy with diffraction
  Link rate assumed
Capacity: Mb/s per cell
  Function of modulation, coding
  Multi-cell scenario
  Cell radius and spectral efficiency assumed
Spectrum efficiency: Mb/s/Hz
Cost
  CPE and cost of installation
  Infrastructure cost per subscriber and cost of coverage
  Cost of spectrum
Product availability

## Slide 3: BeamReach Networks’ Solution
Time Division
Duplexing
Stacked Carrier
Spread
Spectrum
Adaptive
Antenna Arrays
QOS
Enabled
ARQ
OFDM
Adaptive
Modulation
Based on Adaptive MultiBeam OFDM (AMB-OFDM)
  Adaptive beamforming and null steering
Delivers concurrently
  Large coverage
  High link rate
  High capacity
  High spectral efficiency
Low Cost
Launching BeamPlex™ today
No Compromise

## Slide 4: Coverage
Beamforming and Spectral combining
Optimal M-branch diversity combining
  Single antenna at CPE
  < 4 dB fade margin requirements
Huge increase in useable path loss
  Increase in cell area by factor of 16
  Required for indoor installable CPE
Probability Distribution of SNR (dB) for M Branch

## Slide 5: Link Rate & Capacity
Near symmetrical link rates at cell boundaries
  1.5 Mb/s down, net of MAC & PHY overheads
  1.2 Mb/s up
Sub-rate services and settable SLAs
Very high capacity per cell
  Scaleable up to 220 Mb/s in 24 MHz of spectrum
  Thousands of subscribers
  Up to 10 times intra-cell frequency reuse
  Full frequency reuse in adjacent cells

## Slide 6: Spectral Efficiency
Notes: The second and third generation technologies are primarily are designed for mobility systems. However, based on a paper by researchers at Erricson we conclude that even for a fixed system the system capacity would be at most double what is shown here.
Radix’s performance shown is based on a 2x15 MHz layout with 1 MHz guard bands (therefore 2x13 MHz of usable spectrum for data). For a system with 16 antennas and a spectral spreading factor 2, the baseline performance for traffic (4 bits/tone) is 0.92 bps/Hz per user. It is conceivable that the 32 degrees of freedom could support 32 users, in which case the capacity is 29.6 bps/Hz. Although conceivable, supporting 32 users is not likely. Simulations for a single cell indicate that the number of simultaneous users with 32 DOFs is about 16, which corresponds to 14.8 bps/Hz. For an embedded cell with a suburban Hata/COST-231 propagation model, simulations indicate that the number of simultaneous users with 32 DOFs is about 9. This corresponds to 8.3 bps/Hz.

## Slide 7: Performance of AMB-OFDM vs CDMA
Spectral eff.
CDMA: 0.5- 0.75 b/s/Hz
OFDM: 9 b/s/Hz
Capacity
CDMA: 24-27 Mb/s
OFDM: 220 Mb/s
Coverage
CDMA
AMB-OFDM

## Slide 8: Cost of CPE & installation
Typical
Outdoor Install
Radius (miles)
Cell distribution
Indoor Install
Outdoor Install
Outdoor
Indoor
Highly integrated, ASIC based CPE
2 options to minimize truck rolls and maximize cell radius
  All indoor with window mounted antenna
  Mix of indoor and outdoor eaves mounted for larger cell radius

## Slide 9: Infrastructure cost per subscriber

## Slide 10: BeamPlex™ Availability
In local trial: Feb-02
First customer trial in US: Q2-02
Commercial availability: Q3-02
Please come visit us at booth 115

## Slide 11: Conclusions
High link budget & low fade margin
High link rate
High capacity
High spectral efficiency
High spectrum flexibility
All concurrently
Low cost of CPE
Low cost of installation
Low cost of coverage
Low cost of infrastructure
No compromise with BeamPlex™