## Slide 1
Selection of Wavelength for
Free-space Optics Systems
Eric Korevaar
Chief Technology Officer
Optical Access Incorporated

## Slide 2: Outline
The popular free-space optic wavelengths are 785 nm, 850 nm, and 1550 nm
Selection of the laser wavelength is based on
  Non-absorption windows through the atmosphere
  Eye safety
  Atmospheric scattering and scintillation
  Availability and cost of optical components (transmit and receive)
  Data rate
  Cost of active tracking system

## Slide 3: Electromagnetic Spectrum
Smaller carrier wavelength / Higher bandwidth
Spread
spectrum
Microwave
101
102
103
104
105
106
107
108
109
1010
1011
1012
1013
1014
1015
1016
Hertz
kHz
MHz
GHz
THz
107
106
105
104
103
102
10
1
0.1
10-2
10-3
10-4
10-5
10-6
10-7
10-8
Frequency
Wavelength
Radio Waves
Microwaves
Infrared
UV
Power & Telephone
Copper
wire
Trans-
mission
km
meter
cm
mm
m
10-9
nm
1017
Coaxial
cable
Fiber
optic
AM radio
FM radio
Free-space
Optics
c = speed of light
c = f 
c = 3 x108 m/s

## Slide 4: Free Space Optics Wavelength
Wavelength (unit of length) 1 meter = 109 nanometer (nm)
1 wavelength = 
Visible
Spectrum
785
nm
850
nm
1550
nm
FSO wavelengths
400
500
600
700
800
900
1000
1100
1200
1300
1400
1500
1600
1700
Near Infrared
Wavelength (nm)

## Slide 5: Atmospheric Absorption
% transmitted
785
nm
850
nm
1550
nm
400
500
600
700
800
900
1000
1100
1200
1300
1400
1500
1600
1700
Near Infrared
Wavelength (nm)
H2O
O2
H2O
H2O
H2O
H2O
CO2
1300
nm

## Slide 6: Eye Safety
400
500
600
700
800
900
1000
1100
1200
1300
1400
1500
1600
1700
Near Infrared
Wavelength (nm)

## Slide 7: Atmospheric Scattering (Wavelength independent in fog)
Modtran Calculation courtesy of Eric Woodbridge, Air Fiber

## Slide 8
Comparison of Attenuation in 3 fogs
Courtesy of Bob Pierce, TeraBeam Corp.
Calculated Mie Scattering in dB/km for three fog distribution models.

## Slide 9: Atmospheric Scattering
785 nm, 850 nm, and 1550 nm all attenuate at the same rate in fog (visibility < 500 m)
In hazy weather (visibility > 1 km), 1550 nm attenuates less than 785 nm or 850 nm
(Kim, et al. Proc. SPIE, Vol. 4214, 2000)

## Slide 10: Atmospheric Scintillation
Seems to be slightly more atmospheric scintillation at 1550 nm vs 850 nm (Kim, et al. Proc. SPIE, Vol. 3850, 1999)
More scintillation means deeper fades in signal
Slightly more scintillation fade margin needs to be built into 1550 nm lasercom systems
-15.0
-10.0
-5.0
0.0
0
25
9 dB
Time
Receive
Power
(dB)

## Slide 11
Multiple transmitter Patent

## Slide 12
Normalized Intensity (linear)
Time (sec)
3 Apertures
2 Apertures
1 Aperture
Multiple transmitters reduce atmospheric scintillation

## Slide 13
Multiple transmitters reduce scintillation fade margin

## Slide 14
Availability Calculation
Combine Historical Visibility Data with Link range vs. visibility curve to give Availability vs. Link Range curve

## Slide 15
Availability Calculation
TereScope Availability
90
91
92
93
94
95
96
97
98
99
100
0
1
2
3
Link range (km)
Availability (%)
Las Vegas, NV
San Diego, CA
St. Johns, NF

## Slide 16
TereScope Availability Examples

## Slide 17
Comments on Availability
Availability is geographically dependent
This analysis is not precise because of microclimates, but still gives a decent approximation to the availability
Because of conservative link budget numbers, actual availability is generally better than calculated.
Carrier-class availability (99.999%) can be achieved with free-space optics for link ranges up to 200 m in most locations

## Slide 18
Can 99.999% be achieved for longer ranges?
Solution: Free-space optics with an RF back-up
TereScope
Fusion
Hybrid FO/Copper
OptiSwitch Module

## Slide 19
TereScope Fusion Availability

## Slide 20
Lasercom is Protocol Independent
Since laser communication terminals act as simple
repeaters, they are protocol independent. The following protocols have been wirelessly transmitted by laser communication:
  Ethernet, Fast Ethernet, Gigabit Ethernet
  FDDI
  ATM (OC-3 and OC-12)
  ESCON
  OC-48 (2.5 Gbps) and OC-192 (10 Gbps - WDM)

## Slide 21
TereScope™ Family of Free Space Optic Links Product Overview

## Slide 22
TereScopes at a Glance
TereScope 2 Series: E1/T1: 2 Mbps, 500 m to 5 km
TereScope 10 Series: Ethernet - 10 Mbps, 250 m to 3.5 km
TereScope 25 Series: Open Protocol - 1-25 Mbps, 500 to 3 km
TereScope 100 (PAL) Series: Fast Ethernet - 100 Mbps, up to 200 m
TereScope 155 - Protocol Select (PS) Series: 34 - 155 Mbps, 300 to 2.5 km
TereScope 155 - Protocol Independent (PI) Series: 10 - 155 Mbps, 300 to 2.5 km
TereScope 1000 Series: Gigabit Ethernet, up to 500 m

## Slide 23
Large Worldwide Installation Base (Free Space Optics)
USA Canada Mexico Brazil Argentina Uruguay Japan Taiwan S. Korea Philippine Singapore India South Africa Nigeria Australia
Slovenia Croatia Latvia Czechoslovakia Gibraltar Luxemburg Netherlands Norway Greece Germany England Switzerland Sweden Portugal Spain Italy Turkey Israel Saudi Arabia
Sales offices
R&D and Manufacturing

## Slide 24: Optical Components - Cost
785, 850 nm (Optical Access, Air Fiber)
- Transmitter: lasers (25 mW) $30 (Less power but Inexpensive)
- Detector: Si APD’s (25 nW) (More sensitive)
- Visible to Si CCD cameras (for alignment and tracking)
1550 nm (TeraBeam, fSONA)
- Transmitter: EDFA’s (100 mW to 1 W) $10,000 (More power but Expensive)
- Detector: InGaAs APD’s (Less sensitive)
- Not visible to Si CCD camera – need InGaAs quad cell for alignment and tracking
- Can use WDM to rapidly increase bandwidth

## Slide 25
Wavelength and Field of View
Large System Cost Driver is the Use of Active Tracking.
If the Receiver Field of View and Transmitter Divergence are large enough,
Tracking is not generally needed.
Transmitter Divergence is easy to adjust, only affects link budget
Receiver Field of View depends ultimately on Receive Aperture Diameter,
Effective Focal Length and Detector Diameter
For a given bandwidth (data rate), sensitive detectors at 850 nm (silicon APD)
can have a larger diameter than detectors at 1550 nm (InGaAs).
The use of less precise optics and the avoidance of active tracking seems to give
a price advantage to 785/850 nm systems as compared to 1550 nm systems
up to at least Gigabit Ethernet speeds.

## Slide 26
Key Issue for Success of Optical Wireless
COST
Suppliers of Free Space Optical Equipment will not be able to convince
service providers that the system availability will be as high as for fiber optics.
The cost of using FSO must be significantly lower than the cost of using other
alternatives with perceived higher availability, including fiber and millimeter waves.
High bandwidth, eye-safe FSO systems can be manufactured at 785 nm, 850 nm,
1550 nm and other wavelengths with the same link availability and reliability at
a given distance. In the end, price will determine which technologies are successful.