## Slide 1
851 Burlway Road, Burlingame, CA 94010; Phone: (650) 348-1190; Fax: (650) 348-1261; Email: info@swedcom.com
DIRECTIONAL ANTENNA SELECTION AND DEPLOYMENT
Jim Bryant (jbryant@swedcom.com)
UNLICENSED MULTIPOINT OPERATIONS
Strategies for Reducing Interference by Effectively
Evaluating and Deploying Directional Antennas
Presented By: Jim Bryant

## Slide 2
851 Burlway Road, Burlingame, CA 94010; Phone: (650) 348-1190; Fax: (650) 348-1261; Email: info@swedcom.com
DIRECTIONAL ANTENNA SELECTION AND DEPLOYMENT
Jim Bryant (jbryant@swedcom.com)
DEPLOYMENT CONSIDERATIONS
Antenna Elevation and Azimuth Patterns
Base Station Deployment Considerations
Link Budget and Interference
Antenna Electrical Parameters

## Slide 3
851 Burlway Road, Burlingame, CA 94010; Phone: (650) 348-1190; Fax: (650) 348-1261; Email: info@swedcom.com
Elevation Pattern A
Elevation Pattern B
Elevation Pattern C
WHICH ANTENNA WOULD YOU CHOOSE?
DIRECTIONAL ANTENNA SELECTION AND DEPLOYMENT
Jim Bryant (jbryant@swedcom.com)

## Slide 4
851 Burlway Road, Burlingame, CA 94010; Phone: (650) 348-1190; Fax: (650) 348-1261; Email: info@swedcom.com
50 dB Resolution
40 dB Resolution
30 dB Resolution
THEY ARE FROM THE SAME ANTENNA
DIRECTIONAL ANTENNA SELECTION AND DEPLOYMENT
Jim Bryant (jbryant@swedcom.com)

## Slide 5
851 Burlway Road, Burlingame, CA 94010; Phone: (650) 348-1190; Fax: (650) 348-1261; Email: info@swedcom.com
PROPER EVALUATION OF PATTERNS REQUIRES
   40 dB OF PATTERN RESOLUTION
+13
-22
-17
-12
-7
-2
+3
+8
DIRECTIONAL ANTENNA SELECTION AND DEPLOYMENT
Jim Bryant (jbryant@swedcom.com)

## Slide 6
851 Burlway Road, Burlingame, CA 94010; Phone: (650) 348-1190; Fax: (650) 348-1261; Email: info@swedcom.com
COMPARING AZIMUTH PATTERNS
(POWER BEHIND THE ANTENNAS)
Antenna B
Antenna A
DIRECTIONAL ANTENNA SELECTION AND DEPLOYMENT
Jim Bryant (jbryant@swedcom.com)
-90
+90

## Slide 7
851 Burlway Road, Burlingame, CA 94010; Phone: (650) 348-1190; Fax: (650) 348-1261; Email: info@swedcom.com
ISOLATION AT THE BASE STATION
DIRECTIONAL ANTENNA SELECTION AND DEPLOYMENT
Jim Bryant (jbryant@swedcom.com)
0
1
2
3
4
L1
L2
L3
Antenna
Pattern 1
Antenna
Pattern 3
0
0
0
Antenna
Pattern 2
Antenna
Pattern 4
Access Point (Radio)
for Antenna 1
Antenna-to-antenna isolation takes into account all gains and losses in the signal between two radios.
Access Point (Radio)
for Antenna 2
Antenna-to-Antenna
Isolation

## Slide 8
851 Burlway Road, Burlingame, CA 94010; Phone: (650) 348-1190; Fax: (650) 348-1261; Email: info@swedcom.com
DIRECTIONAL ANTENNA SELECTION AND DEPLOYMENT
Jim Bryant (jbryant@swedcom.com)
Transmit
Power
(30 dBm)
Receiver
Threshold
(-85 dBm)
ISOLATION AT THE BASE STATION
Noise Floor
(-90 dBm)
The ideal antenna-to-antenna isolation level should produce a noise level that is less than the manufacturer’s stated radio receive sensitivity.
30 dBm - (-90 dBm) = 120 dBm

## Slide 9
851 Burlway Road, Burlingame, CA 94010; Phone: (650) 348-1190; Fax: (650) 348-1261; Email: info@swedcom.com
If the worst-case antenna-to-antenna isolation at your base station is 100 dBm, then your actual (or highest) noise floor can be calculated.
DIRECTIONAL ANTENNA SELECTION AND DEPLOYMENT
Jim Bryant (jbryant@swedcom.com)
Transmit
Power
(30 dBm)
Receiver
Threshold
(-85 dBm)
Highest Noise Floor
(-70 dBm)
Noise
Floor
(-90 dBm)
ISOLATION AT THE BASE STATION
30 dBm - (100 dBm) = -70 dBm

## Slide 10
851 Burlway Road, Burlingame, CA 94010; Phone: (650) 348-1190; Fax: (650) 348-1261; Email: info@swedcom.com
The lowest possible signal power at the receiver will need to be higher if the actual noise floor at the base station is greater than the manufacturer’s stated radio receive sensitivity.
DIRECTIONAL ANTENNA SELECTION AND DEPLOYMENT
Jim Bryant (jbryant@swedcom.com)
Transmit
Power
(30 dBm)
Minimum PR
(-65 dBm)
Receiver
Threshold
(-85 dBm)
Highest Noise Floor
(-70 dBm)
Noise
Floor
(-90 dBm)
ISOLATION AT THE BASE STATION
-70 dBm + (5 dBm) = - 65 dBm

## Slide 11
851 Burlway Road, Burlingame, CA 94010; Phone: (650) 348-1190; Fax: (650) 348-1261; Email: info@swedcom.com
Distance “L”
Radio
Gain (GT)
With the minimum value for PR (received signal power) known at the base station, the radius of your cell can be calculated by using the standard link budget formula.
DIRECTIONAL ANTENNA SELECTION AND DEPLOYMENT
Jim Bryant (jbryant@swedcom.com)
COVERAGE AREA
Base Station
Customer Premise
Access Point
Gain (GR)
Transmit
Power
(30 dBm)
Minimum PR
(-65 dBm)
30 dBm - (-65 dBm) = 95 dBm > all gains and losses in the signal between the two radios

## Slide 12
851 Burlway Road, Burlingame, CA 94010; Phone: (650) 348-1190; Fax: (650) 348-1261; Email: info@swedcom.com
INTERFERENCE CONSIDERATIONS
1
2
L
Top View
L
Antennas are at Same Height
DIRECTIONAL ANTENNA SELECTION AND DEPLOYMENT
Jim Bryant (jbryant@swedcom.com)

## Slide 13
851 Burlway Road, Burlingame, CA 94010; Phone: (650) 348-1190; Fax: (650) 348-1261; Email: info@swedcom.com
DIRECTIONAL ANTENNA SELECTION AND DEPLOYMENT
Jim Bryant (jbryant@swedcom.com)
DOWN TILTING AN ANTENNA
Reduce the amount of interference from external sources.
Improve the link between your base station and your customers.
No Tilt (Elevation Pattern Shown)
With Tilt
Your Base Station
Your Base Station
External Source
External Source
Antenna
Antenna
Antenna
Antenna

## Slide 14
851 Burlway Road, Burlingame, CA 94010; Phone: (650) 348-1190; Fax: (650) 348-1261; Email: info@swedcom.com
DIRECTIONAL ANTENNA SELECTION AND DEPLOYMENT
Jim Bryant (jbryant@swedcom.com)
DOWN TILTING AN ANTENNA
Reduce the amount of interference from external sources.
Improve the link between your base station and your customers.
Your Base Station
Before Tilt (Shown in Black)
After Tilt (Shown in Green)

## Slide 15
851 Burlway Road, Burlingame, CA 94010; Phone: (650) 348-1190; Fax: (650) 348-1261; Email: info@swedcom.com
MOUNTING CONSIDERATIONS
When mounting an antenna on an object such as a pole and/or a building, be sure to consider movement of the object(s).
A + B « Vertical Beamwidth
( B)
Movement
of Pole
( A)
Movement
of Building
DIRECTIONAL ANTENNA SELECTION AND DEPLOYMENT
Jim Bryant (jbryant@swedcom.com)

## Slide 16
851 Burlway Road, Burlingame, CA 94010; Phone: (650) 348-1190; Fax: (650) 348-1261; Email: info@swedcom.com
ANTENNA ELECTRICAL PARAMETERS
Gain
Front-to-Back Ratio
Azimuth Patterns
Elevation Patterns
Upper Lobes
Return Loss
Tilt
The following electrical parameters will change
over an antenna’s designed bandwidth:
DIRECTIONAL ANTENNA SELECTION AND DEPLOYMENT
Jim Bryant (jbryant@swedcom.com)

## Slide 17
851 Burlway Road, Burlingame, CA 94010; Phone: (650) 348-1190; Fax: (650) 348-1261; Email: info@swedcom.com
DEPLOYMENT CONSIDERATIONS
Understand the Ramifications of Various Resolutions on Patterns.
Consider All Points on an Azimuth and Elevation Pattern.
Ensure Proper Isolation Between Antennas at Base Station.
Perform a Worst Case Link Budget.
Calculate Worst Case Interference from Neighboring Antennas.
Down Tilt When Possible.
Take into Account Movement of the Object(s) the Antennas are Mounted to.
Know How the Antenna Parameters Change Over the Bandwidth.
DIRECTIONAL ANTENNA SELECTION AND DEPLOYMENT
Jim Bryant (jbryant@swedcom.com)