## Slide 1: A Brief Review of 5Ghz Wireless Standards
Ken Haase
Proxim
February 2002

## Slide 2: Wireless Data “Standards” Alphabet Soup
DECT
SWAP
802.15
802.11IR
802.11FH
Bluetooth
OpenAir
HomeRF
IEEE
CDPD
802.11a
WLIF
GSM
3G
802.11DS
HiperLAN1
PHS
TR41.2
IS95B
HiperLAN2
802.11b

## Slide 3: 5 GHz Frequency Band
Referred to in U.S. as Unlicensed National Information Infrastructure (U-NII) band
Divided into three (3) sub-bands
  Proxim to support low- and mid-band
    Low-band (5.15 - 5.25 GHz)
    Mid-band (5.25 - 5.35 GHz)
    High-band (5.725 - 5.825 GHz)
Different output power limits and antenna type limitations in each band
802.11a presently certifiable in FCC-based regions and Japan (specific frequency range)
  Europe 5 GHz band currently reserved for HiperLAN/2-compliant products
  Coordination efforts underway between standards and regulatory bodies to certify 802.11a in Europe

## Slide 4: Unlicensed 5GHz Spectrum
Integral antennas only

## Slide 5: Performance Interference Free 5Ghz - A Clean Band
No interference from microwave ovens, Bluetooth, legacy wireless LANs or cordless phones
2.4 GHz
5 GHz
Bluetooth
Microwave Ovens
DS and FH Wireless LANs
Cordless phones
Clean Air

## Slide 6: HiperLAN/2 ETSI 5 GHz Wireless Standard
Spectrum: 5 GHz, OFDM
Data Rates: 54 Mbps, with fallback rates from 36 to 6 Mbps
Throughput: Efficiency exceeds 50% with small number of users, but declines due to scheduling overhead for large number of users.
Certifiability: Worldwide
Benefits
  TDM based QOS architecture good for distribution of high quality video
  Dynamic Frequency Selection reduces interference between multiple access points.
  Transmit Power Control adjusts power to lowest level needed for link quality
  Worldwide certifiability
Issues
  No products in the market
  Few developers, no broad support
Notes: * HiperLAN2 uses an almost identical PHY to 802.11a.
* The HiperLAN2 MAC has a connection-oriented protocol (similar to ATM)
* Every session must be set up and torn down, prior to exchanging data.
* The connection orientation while good for constant rate traffic like video
will likely prove Inefficient for Ethernet based applications, using IP protocols
* Standard does not support Ad-hoc (peer-to-peer) connections.
* Applications requiring QOS are also being addressed today
using connection-less protocols with packet shaping software.
Proxim view:
* HiperLAN-2 may prove to be a good solution for distributing digital TV
signals within the home.
* HiperLAN-2 may be too late to market to achieve penetration rates
required to become competitive with 802.11a

## Slide 7: HiperLAN2 Appears To Be Losing Momentum
HiperLAN2
  http://news.zdnet.co.uk/story/0,,t284-s2101101,00.html
  “Ericsson, one of the leaders of the HiperLAN movement, has pulled out of that effort, effectively signalling its demise before products came to the market in any serious way.
  "We see the market as moving to 802.11a. Our focus is on 802.11a now," said an Ericsson spokesman.”
Is this the end of HiperLAN2?

## Slide 8: IEEE 802.11a The NEXT Enterprise Wireless LAN Winner
Spectrum: 5 GHz; OFDM
  Channels: 12 non-overlapping (4 in each of three bands)
Data Rates: 54 Mbps standard
  Proxim 2X mode: 108 Mbps
Throughput: 23 Mbps @ 54 Mbps standard rate
  34 Mbps @ Proxim 108 Mbps rate
Certifiability: US and Japan;
  Europe will be addressed through 802 .11h proposal
Benefits
  Wireless can compete in speed/capacity with wired solutions
  Avoids interference from microwave ovens, cordless phones
Issues
  Dynamic Frequency Selection and Transmit Power Control must be added to sell products in Europe
Notes: 802.11h proposal addresses coexistence of 802.11a with HiperLAN/2
ERC DEC 99 defines frequency bands, power limits, coexistence mechanisms
.11h Adds Dynamic Channel Selection (DCS)
  Sense receiver idle channel signal strength to detect interference
  Automatically configure frequency channel to avoid interference
  AP controls the process, Clients follow the AP command
.11h Adds Transmit Power Control (TPC)
Proxim View:
  Proxim will pursue regulatory approval for its 802.11a products in Europe
  based on DCS and TPC features in its initial product.
  Proxim will build .11h compliance into its products
  when final issues with the standard are decided.

## Slide 9: All the Speed you Need 802.11a Fast Wireless Ethernet
Up to 100 Mbps wireless networking in conference rooms, classrooms, public hot-spots
Selectable between 802.11a mode for interoperability up to 54 Mbps, and 2X for data rates up to 108 Mbps
Example usage scenario:
  Two high-quality video streams (~10 Mbps) + Four high-quality audio streams (~1 Mbps) + ~14 Mbps for data
802.11a
802.11b
54
108
11
Proxim
2X mode

## Slide 10: All the Speed You Need Better Performance at Any Range
802.11a retains consistently higher data rates than 802.11b at all distances
More robust modulation techniques
Forward error correction
All values are radio rate in Mbps
Not all radio rates are shown

## Slide 11: PC Magazine 11a vs. 11b Comparison
“In data-transfer testing, we found that the Proxim 802.11a cards were up to about 4.5 times as fast as the 802.11b cards.”
PC Magazine, December 11, 2001

## Slide 12: 802.11a Spectrum and Channel Allocation
20 MHz channel is divided into 52 carriers (48 carry data, 4 are pilot signals)
All 52 carriers are always used and each carrier is ~300kHz wide
Data rates from 6 Mb/s to 54 Mb/s are supported by varying modulation and error correction coding
...
20 MHz
52 Carriers total
One Channel (detail)
Eight channels in lower 5 GHz band
Each carrier is ~300kHz wide
5150
5350 MHz
5180
5200
5240
5280
5300
5220
5260
5300

## Slide 13: OFDM Advantages Orthogonal Frequency Division Multiplexing (OFDM)
Transmits more data, more reliably
  Multi-channel modulation sends a lot of information in a short time
  Higher data rate means greater bandwidth utilization due to reduced on-air time per transmission
  Incorporates Forward Error Correction (FEC) to increase transmission accuracy
Superior multipath tolerance
  Over 10x greater tolerance to reflected signals than 802.11b
    800 ns delay tolerance for 802.11a vs. 65 ns for 802.11b
  Increases reliability in challenging environments (offices, warehouses, residences, etc.)

## Slide 14: Thank you! Ken Haase Director of Product Marketing Proxim Inc. khaase@proxim.com www.proxim.com