## Slide 1: Voice QoS in IP-Centric BWA Systems
Engineering Toll-quality voice into IP BWA
Michael Stumm
SOMA Networks
February 14, 2002

## Slide 2: Toll-quality Voice: Critically Important for BWA Networks
Premise:
Toll quality voice is critical to make the business case work for the new generation, non-line-of-sight, residential Wireless Broadband Access solutions.
The name of the game is revenue generation

## Slide 3: Revenue per user per month
0.00
20.00
40.00
60.00
80.00
100.00
120.00
Monthly Revenue/User in USD
Web services
Long Distance
Calling Features
Local Voice
Residential Data
$44.35
$10.00
source: Goldman Sachs Equity Research, FCC, Verio Web Hosting
ILEC
DLEC and CATV
IXC
Data
$44.35
$22.24
$9.99
$21.00
$10.00
vs.
Voice & Data
Voice is a killer IP app if toll-quality + features
Notes: :: add notes: would discount on line charges as beachead and make money on features

## Slide 4: Layering a standard VoIP protocol ain’t gonna cut it
Thesis 1:
Simply layering a VoIP protocol, such as H.323 or SIP, over a data-oriented IP pipe is not a suitable solution, as it either
will not have the required quality, or it
will not be cost-effective

## Slide 5: Basic Problem: contention is the norm
Home Network
Packet Core
PSTN
Public Internet
Bandwidth:
Bandwidth over the air is the critical resource
limited, expensive resource that must be managed efficiently

## Slide 6: Layering a standard VoIP protocol ain’t gonna cut it
Thesis 2:
Voice has to be engineered into all layers of communication --- it cannot be added as an after-thought!
Air Interface
Link
IP
TCP/UDP
RTP
Application: VoIP: H.323 / SIP / Etc.

## Slide 7: Air Interface QoS issues
Key Issue:
Needed:
IP data traffic different than voice traffic
Traditional Telco View
Internet View
Hybrid with
  Dynamic channel resizing
  Powerful RRM
  Higher-density modems

## Slide 8: Air Interface QoS issues (cont.)
Issue:
Nice:
Voice has higher tolerance for bit errors than data
Reduce ARQ and FEC overheads for voice only

## Slide 9: Link layer QoS issues
Key Issue:
Needed:
Large IP packet can unacceptably delay voice packets
Packet preemption, fragmentation and reassembly at link layer
Example:
200 Kbps uplink: one 1,500 byte packet can delay voice packet by 60 ms
= 1/3 of 200 ms end-to-end delay budget

## Slide 10: Link layer QoS issues (cont.)
Packet headers too expensive for voice
Heavy duty header compression for voice
Voice: down to 2 bits
Key Issue:
Needed:
Good vocoder: 8 Kbps: 1 packet / 10 ms 80% Overh.
1 packet / 20 ms 66% Overh.
header
header
Bytes: 40 10
Bytes: 40 20

## Slide 11: IP layer QoS issues
Issue:
Needed:
Issue:
Needed:
TOS byte cheaters (I.e. teenagers playing Quake, etc.)
TOS byte monitoring and control Differentiate voice from data
Queuing policy is critical
Differentiated IP queuing treatment for voice, 911, system, mgmt, and user data packets

## Slide 12: Application layer QoS issues
Issue:
Needed:
Issue:
Needed:
How to exploit application-layer knowledge to maximize efficiency
Capability to make intelligent QoS-related requests of underlying layers
How to have lower layers influence application
Integrated strategy
Interplay between application and network layers
Consider:
switch from 8 to 64-bit vocoder for FAX or modems
having 911 calls preempt an existing call
Consider: AI layer requesting application to cut vocoder rate in 9/11 or X-mas congestion situations

## Slide 13: The bottom line
It’s not:
It’s:
Bits / hz
Profit / Hz
= (bits/Hz)*(revenue/sub) / (bits/sub) – (cost/Hz)
maximize spectral efficiency for highest capacity (bits/Hz)
maximize revenue/bit with high-margin services like voice (revenue/sub)
minimize bandwidth per sub for delivered services (bits/sub)
minimize overall system costs (cost/Hz)

## Slide 14: Voice is a killer IP application . . .
Voice, if done right (i.e. toll-quality + features), can generate 50% of revenue, but only costs 5% of bandwidth.
. . . but it is not easy
Issue:
Worst case delay budget is 200 ms., considering:
vocoder processing delays
packetization delays
queuing delays
modem delays
radio frame wait time
serial transmission time
router and switch forwarding delays
receive jitter buffer delays
PSTN delays

## Slide 15: SOMA’s Amosphere: cost-effective toll-quality Voice + Data
SOMA’s Amosphere addresses this challenge:
  max 100 ms voice delay between CPE and PSTN
  max 200 ms voice delay between two Amosphere CPE’s
with large efficiency gains over competing solutions:
  +50% for air interface coding tailored to voice
  +50% for VAD + CNI + CDMA
  +25% for extreme header compression
  +15% for distributed (localized) intelligence to collect digit, generate dial, ring, and busy tones, and the processing of announcements, speed-dialing, call forwarding call-screening
Efficiency gain factor of 6
6 times more subscribers
600% increase in voice revenue

## Slide 16: SOMA Meets the Six Requirements for Profitability
no truck rolls
Self-steering antenna design
Non-line-of-sight
Handles building penetration loss
facilities-based
toll-quality voice
self-provision & self-serve
rapid, low-cost feature delivery
broadband data
Internet-era technology
Web and VoiceXML IVR tools
Over-the-air service activation
AmosTM service creation and execution environment
Breakthrough capabilities
Radically open API + SDK
Unified transport, control, and signal processing
Megabit Internet access
Multiple PCs
Future advanced services
Built-in ground-up
Regular POTS phone
QoS from air to app
High availability
State-of-the-art SAI radio
Paired 5MHz spectrum
1:1 frequency reuse