## Slide 1: Unlicensed Multipoint Operations
UNII Band: Reliability, Interference and Economic Viability
Robert A. Campbell
rcampbell@nscg.biz

## Slide 2: Reliability
What does it mean?
  Uptime 99.999%?
    <5 minutes downtime each YEAR
  Operating in spite of weather, environmental or other characteristics?
  Or does it just simply work?

## Slide 3: 99.999%
Translates roughly to 5 minutes 15 seconds of downtime per YEAR
  That’s 6 SECONDS per week
If you have a single outage of 2 hours, you will need 100% uptime for the next 23 years to achieve 99.999%
Unachievable? Maybe Good Idea? Absolutely
FACT: This is an ideal goal that is rarely met, but striving to meet it provides great benefits.
A lot of issues can be out of your control

## Slide 4: UNII and the Environment
UNII band, outdoors, frequency range 5.25GHz-5.35GHz and 5.725GHz-5.825GHz
Below 6GHz water and other weather phenomenon are not a concern
Given FCC regulations limit an effective transmission range to approximately 7 miles, curvature of the earth is generally not a concern
Lightning is one of our biggest concerns along with improperly terminated cables (which can be affected by weather)
Bottom Line: The Environment can be managed

## Slide 5: Interference
RF Interference or Electromagnetic Interference (EMI)
Huge impact on reliability
UNII Band – 200MHz of spectrum ISM 2.4GHz – 83.5 MHz of spectrum
Most equipment available has sufficient channel plans to allow for multiple operators in the same RF space – the channel plan
Equipment vendors are beginning to build interference mitigation into their products
  If you know what you’re sending and have a good idea on what you’re to receive, then block anything else

## Slide 6: Interference
802.11a – new kid on the block
  Current target: Indoor Wireless LAN, could change
  Using indoor-only frequencies (5.15GHz – 5.25GHz) along with 5.25GHZ-5.35GHz
Plan the network, survey the RF landscape, document your network
Legal recourse for malicious interference, but no recourse for other interference
  Back to the equipment’s ability to reject interference as the landscape crowds

## Slide 7: Does it work?
Obviously, YES! You’re here aren’t you? 
Shipping equipment with deployments and real world feedback have shown that equipment vendors are putting out quality products

## Slide 8: Economic Viability
Viable models
  Urban: Augmenting Fiber as it isn’t in every building
  Suburban: Where is the business? Underserved? Extending the Urban reach?
  Rural: Difficult due to ranges of equipment, but more cost effective in low density markets than anything else

## Slide 9: Know what you’re getting into
Urban Markets
  Incumbent Fiber and copper-based carriers
  Incumbent DSL, Cable Modem and low-cost point-to-point DS1/DS3 connections
  High-cost of operations related to rooftops/tower leasing – permitting requirements
  Partnering is one answer
  Addition of vertical services is key to maintaining value proposition

## Slide 10: Viability
Suburban Markets
  Areas where infrastructure is limited
  Outside the DSL areas and access to copper or fiber is limited
  New business centers that need connectivity abound
  More of the “underserved” area clients
  Still, vertical services would increase the penetration into market (VoIP, VPN, etc.)
  Access to rooftops and/or towers at lower rates

## Slide 11: Viability
Rural Markets
  Cost of wireless equipment doesn’t require high-density of population, but minimums needed to satisfy model
  “Small Town USA” needs bandwidth
    Some argue it is needed here more because of a lack of access to metro market services
  Range of equipment can present coverage problems for UNII deployment
  Despite this, success stories exist in “one-stoplight” towns

## Slide 12: Viability
Market size
FCC report: Broadband = >200Kbps
  Approximately 9.6 million high-speed subscribers as of June 30, 2001
  A 250% increase since the FCC released its Second Report
  A 36% increase during the first half of 2001
  7.8 Million (of 9.6 Million) subscribers are residential or small business
Source: www.fcc.gov/Bureaus/Common_Carrier/News_Releases/2002/nrcc0201.html

## Slide 13: Viability
Good news for fixed wireless
“High-speed lines in service over satellite or fixed wireless technologies increased at the fastest rate, 73% during the first half of 2001, to nearly 200,000.”
Source: www.fcc.gov/Bureaus/Common_Carrier/News_Releases/2002/nrcc0201.html

## Slide 14: Conclusion
UNII Band equipment can and does provide more than adequate service and transport of advanced services
Spectrum is not that crowded, yet
Market size is still small, penetration rates growing rapidly
Fantastic opportunities for those who plan and execute now