## Slide 1
Business Model with 2nd 4th Generation
Wireless Access Technology
Bob Kelsch- President
Broadband Wireless World Forum
February 12-14, 2002
Anaheim, CA

## Slide 2: Outline
Requirements for high return business model
4th Generation Technology
System performance
Business Model
Conclusions

## Slide 3: Requirements for high return business model
Low cost, customer installable CPE
  Eliminate installation costs, rapid service deployment
Low cost of coverage
  Macro-cell with > 4 miles radius
  Non line-of-sight performance with >90% coverage
  High link budget (> 150-160 dB) & low fade margins (<5 db)
Low cost per sub for infrastructure
  Large base station capacity = 1000’s of subscribers
Low Spectrum Costs
  High spectral efficiency and flexibility in spectrum use
Business and residential service support
  Symmetric links
Potential for additional revenues:
  Voice services
  Home Networking

## Slide 4: Adaptive MultiBeam OFDM™ Technology
Seamless integration of technology elements
Delivers superior
Coverage
Capacity
Cost
Service Delivery
Time Division
Duplexing
Stacked Carrier
Spread
Spectrum
Adaptive
Antenna Arrays
QOS
Enabled
ARQ
OFDM
Adaptive
Modulation

## Slide 5: Adaptive Beamforming and Null Steering
Beamforming improves system gain, extending cell radius
Adaptive algorithms maximize signal to interference and noise ratio (SINR)
Optimal combining provides spatial diversity, reducing fade margin
Short multipath delays are combined coherently, improving SINR
Null Steering rejects co-channel interference, enabling full frequency re-use
Remote Unit
Out-of-cell Interference
Short delay multipath source
Null Towards Interferer
Gain Towards
Desired Signal
Multipath
combined
coherently
Beam formed adaptively to maximize SINR

## Slide 6: Adaptive Multi-Beam
Concurrent adaptation of multiple independent beams
Multiple users supported at the same time on the same frequencies
  Common antennas and transceivers at the base station
Full inter-cell reuse (N=1) and intra-cell reuse factor of 10
Remote 1
Remote 2
Remote 3
Remote 1
Remote 2
Remote 3
Out-of-cell Interferer
Nulling
out-of-cell Interferer
Multiple users on the same frequency at the same time

## Slide 7: Adaptive Multi-Beam with Stacked Carrier Spread Spectrum
Signals adaptively spread over multiple frequencies
Allows discrimination between users on the same azimuth
Reduces susceptibility to frequency-selective fading
Diversity at CPE without multiple antennas and radios
Spatial & Spectral Beamforming
M antennas, 2 frequencies
2M degrees of freedom
Use of 2 Frequencies Enables
Range-Based Discrimination
Combined spectral/spatial
beamforming delivers
a spot beam to each user

## Slide 8: Adaptive Multi-beam with TDD
With TDD, forward and reverse link channels are “reciprocal”
Blind adaptive algorithms operate at base station and CPE
Spatial beams and nulls are formed in both directions
Single antenna and RF chain provides lowest cost CPE solution
Reciprocal
Channel
uplink spread
UP
DOWN
uplink despread
downlink spread
downlink despread
Adaptive
loop
Adaptive
loop

## Slide 9: Unique Propagation Advantages
Beamforming and Spectral combining gain adds 6 to 10 db to link budget
Optimal M-branch diversity combining reduces fade margin required by 5 to 15 db
Combined link budget advantage is 11 - 25 db in typical deployments
Increased coverage & link reliability
  Cell radius by factor of 2 to 4
  Cell area by factor of 4 to 16
Required for deployment of indoor customer installable CPE

## Slide 10: Spectral Efficiency

## Slide 11: City Model- Assumptions
Population: 1,250 K
Households: 520 K
Businesses: 10%
Area: 2300 Sq.Mi.
Households/Sq. Mi.: 225
Year 1
Year 2
Year 3
Year 4
Year 5
Household served (%)
2%
6%
11%
16%
20%
Number of residential subscribers
9,700
26,700
53,300
72,700
92,100
Number of business subscribers
984
2,625
4,921
7,218
9,187
Service Roll-out

## Slide 12: Assumptions (cont’d)
Residential
Business
Service
(1.5 Mb/s / 1.2 Mb/s)
$ 49/ mo
$ 79/ mo
CPE revenue
$100
$200
Installation Revenue
$0
$240
Revenues
  Only 4x 6 MHz channels required
  4 mile cell radius
    Base station antenna height:100ft
    90% coverage, 99.99% availability
  Customer acquisition: $125 per addition
  Customer service & billing: $7/ mo/ sub
  Overhead: $9/ mo/sub

## Slide 13: Infrastructure cost per subscriber

## Slide 14: Comparison to DSL- Results
IRR: 39% for BeamReach solution vs 16% for DSL

## Slide 15: Conclusions
High return business case with superior economics to DSL
  Concurrently supports large coverage and large capacity
  Lowest infrastructure costs
    Lowest capital requirements
  Low cost, customer deployable CPE
  Superior IRR
No compromise with BeamPlex™