## Slide 1: Delivering NLOS Wireless Broadband Using CDMA-Based Solutions
Roger Quayle, CTO
February 2002
Proprietary and confidential - subject to nondisclosure agreement

## Slide 2: Today’s Discussion
Why CDMA?
Not all CDMA is created equal
International Standards compliance
Why UMTS TD-CDMA?
Optimization of UMTS TD-CDMA
IPWireless implementation
Benefits – coverage, throughput, mobility etc.

## Slide 3: Why CDMA?
Strong international standards
Selected over other candidates (TDMA, OFDM) for UMTS 3G standards
Waveform is noise-like
Spread-spectrum
  Immunity to interference
  Negative C/I performance – permits n=1 reuse
  Flexibility in spreading, coding, modulation
Orthogonality
  Code channels mutually non-interfering

## Slide 4: Not all CDMA is Created Equal
Cdma 2000 1X
  Good technology, evolution from IS-95
  Limitations imposed by narrow channels, legacy support
  Not accepted in European market
UMTS TD-SCDMA (Chinese version, low chip rate)
  Low chiprate (narrow channel) limits broadband application
  Synchronous uplink no use in non-LOS multipath channel
  Limited acceptance outside of Chinese market
Proprietary CDMA
  Loses standards benefits
  Tend to be less sophisticated in systems context
UMTS TD-CDMA high chip rate

## Slide 5: UMTS TD-CDMA (HCR)
UMTS designed from the outset to serve fixed portable and mobile environments
UMTS is inherently broadband – wideband CDMA, wide channel bandwidths supported
Mobile technology model - inherently enables non-LOS, self-installation, roaming, handoff
TDD
  Flexible TDD structure ideally suited to packet data services
  Allows operation in fragmented spectrum allocations
  Symmetry adjustment to match Internet traffic (asymmetric)
Industry wide R&D
Huge economies of scale
International market – not limited to North America

## Slide 6: Optimizing UMTS for Broadband Internet Access
Standard sets minimum targets for performance
  Performance can be increased while maintaining full standards compliance, using advanced signal processing
IPWireless has chosen 3GPP TD-CDMA
  Flexible TDD structure ideally suited to packet data services
  Higher data rates relative to 3GPP FDD
Fully IP based Core Network
UMTS Radio Access Network
  3GPP Shared Channel concept fully exploited
  Statistical multiplexing allows higher cell throughputs
Optimized TD-CDMA for Broadband Internet access
  Powerful link budget – supports large cells
  Downlink throughput up to 8 Mbps at 7.68Mcps
  UMTS release 5 increases to >16 Mbps

## Slide 7: IPW Optimization Techniques
Orthogonal multi-code transmission
  Increases capacity of radio channel (orthogonal code channels mutually non-interfering)
  Multiplies throughput for high speed packet data services
Joint Detection
  Restores orthogonality between codes in a multipath environment, effectively “canceling” interference
  Deals with near-far effect of multiple CPE
  Constructively combines multipath, turning multipath to an advantage

## Slide 8: UMTS in Non-Line-of-Sight Operation
Non-LOS operation requires:
  High system gain to counteract pathloss and building penetration loss, and
  Ability to deal with multipath
Non-LOS operation is inherent in UMTS
  A fundamental requirement for mobile and portable operation
  UMTS 30-03 ‘channel B” specifies a 6 path model, each path individually Rayleigh faded, with a multipath delay spread up to 4 microcesonds
3GPP TD-CDMA solution from IPWireless:
  Achieves high system gain through orthogonal multicode and joint detection
  Constructively combines multipath, increasing effective receiver sensitivity (function of joint detector)

## Slide 9: Constructive Combining of Multipath Using Joint Detection
Power
Time

## Slide 10: Portability and Mobility
UMTS supports fixed, portable and mobile environments
  fundamental requirement to support high speed mobility
  portable and fixed operation comes for free, and with higher throughputs
Necessary techniques for coping with high speed are inherent in the standard
  Radio Frame and Burst Structure
  Transport Channel Processing
    Interleaving, FEC, Rate Matching, etc.
Automatic cell selection / reselection and handoff
The IPWireless TD-CDMA solution supports mobility at 70mph (as per standard), and in practice higher

## Slide 11: Further Enhancements
UMTS HSPDA (high speed downlink packet access)
  Higher order modulation, additional coding steps
  Allows users in good C/I conditions fully utilize capability of radio channel
  Downlink rates up to 16 Mbps
Smart Antennas in UMTS
  Key is to first have a powerful air interface that can achieve maximum performance through signal processing – better to achieve performance in silicon than in “ironwork”
  UMTS supports smart antennas as an enhancement, IPWireless plans to implement in accordance with standards
  Smart antennas have most benefit in capacity (reduced C/I) rather than coverage (as proven in cellular implementations)

## Slide 12: Economy of Scale in Serving Multiple Markets
With UMTS (such as IPWireless), an operator enjoys the economies of scale of a single infrastructure investment serving multiple market sectors
Fixed
Portable
Mobile
UMTS TD-CDMA Network

## Slide 13: Summary
Wideband CDMA provide the most powerful and flexible foundation for broadband wireless
TD-CDMA branch of UMTS is best for high speed packet data, TDD advantageous in fragmented spectrum
Non LOS operation inherent in UMTS TD-CDMA
Mobility and portability inherent in UMTS TD-CDMA
UMTS provides a level of sophistication and performance which cannot easily be duplicated
International standards essential for major worldwide success