## Slide 1: 2nd Generation Wireless LAN Opportunities and Mass Adoption Challenges
Atheros Communications, Inc. | www.atheros.com
Feb 13, 2002 – Broadband Wireless World Forum
Sheung Li
Product Line Manager
sheung@atheros.com

## Slide 2: Wireless Data Delivery Alternatives
WAN, Licensed Band
  2.5G, 3G
2.4 GHz Unlicensed Band
  802.11b
  Home RF
  Bluetooth
5.0 GHz Unlicensed Band
  802.11a
  HiperLAN2, HiSWANa
Proprietary, Non-Standard, Unlicensed Band
  UWB

## Slide 3: Wireless Data Delivery Alternatives
WAN, Licensed Band
  2.5G, 3G
2.4 GHz Unlicensed Band
  802.11b
  Home RF
  Bluetooth
5.0 GHz Unlicensed Band
  802.11a
  HiperLAN2
Proprietary, Non-Standard, Unlicensed Band
  UWB
Wi-Fi
Aka . . .
Wi-Fi5

## Slide 4: Predictions, Myths, and Assertions I
802.11 is the clear winner (Wireless Ethernet)
  Wireless Ethernet is familiar, IP based, immediately useful
  Widely supported, deployed on access points and stations
  Available for computing, consumer electronics, telematics apps
HiperLAN2, HiSWANa will not be volume markets
  Clinging to existence with QoS and DFS/TPC
  Complex ($, wireless ATM), late, centralized control
  Major European, Japan manufacturers now 802.11 supporters
HomeRF is overshadowed
  HomeRF 2.0 is too little, too late
  Intel has dropped support
Bluetooth is for personal area networks
  Bandwidth, efficiency, system capacity limited
Unlicensed Winner: 802.11

## Slide 5: Predictions, Myths, and Assertions I
802.11 is Everywhere
Consumer Electronics
Vehicular
Computing

## Slide 6: WLAN Data Attractiveness
 | WLAN | 3G
Available Spectrum | 383.5 MHz+ (US) Unlicensed | 120 MHz (US) Licensed
Data Rates | 54 Mbps per link max 20 MHz channels ___ | 2 Mbps per link max 5 MHz channels
Power Consumption | 139 Gb/Wh (54Mbps @ 1.4W peak) | 0.036 Gb/Wh (2G) (14Kbps @ 1.3W peak)
Cost | Basestation ~$150 & dropping | A bit more costly …
Status | In laptops, PDAs, home, enterprise, public access | Deployment just beginning
Notes: Spectrum cost in the billions of $$

## Slide 7: The Future is in 5 GHz
2.0
2 GHz Spectrum
2.1
2.2
2.3
2.4
2.5
2.6
2.7
2.8
2.9
3.0
5.0
5 GHz Spectrum in U.S.
5.1
5.2
5.3
5.4
5.5
5.6
5.7
5.8
5.9
6.0
5.0
5 GHz Spectrum in Europe
5.1
5.2
5.3
5.4
5.5
5.6
5.7
5.8
5.9
6.0
5.0
5 GHz Spectrum in Japan
5.1
5.2
5.3
5.4
5.5
5.6
5.7
5.8
5.9
6.0
New Allocation for
Vehicular (Telematics) Applications

## Slide 8: Comparing 1st and 2nd Gen WLAN
 | 802.11b Wi-Fi | 802.11a Wi-Fi5
Data Rate per Channel | 1 – 11Mbps | 6 – 54Mbps
Frequency of Operation (US) | 2.40-2.4835GHz | 5.15-5.35GHz, 5.725-5.825GHz
Available Bandwidth (US) | 83.5MHz | 300+MHz
Number of Non-Overlapping Channels | 3 | 12
Modulation Type | DSSS | OFDM

## Slide 9: Modulation Techniques: 802.11a, 802.11b
1.00s / 0.72s
DSSS / CCK (1-8 bits/seq)
802.11b
20 MHz
OFDM (52 sub-carriers)
...
802.11a
BPSK
QPSK
16QAM
64QAM
1/2, 2/3, 3/4-rate convolutional code
Reduced complexity
Increased performance
BPSK
QPSK
Comparing 1st and 2nd Gen WLAN

## Slide 10: Modulation Techniques: 802.11a, 802.11b
11g Draft Standard
Mixed mode operation
How the 11g Draft Works
SIFS
+
Data
+
SIFS
+
ACK
+
CTS
+
CW
RTS
SIFS
+
+
DIFS
+
11b compatibility
OFDM payload

## Slide 11: Support More Users at 5 GHz
Europe
19 channels
Throughput (Mbps/network)
US
3 channels
50
US
12 channels
500
100
300
Japan
4 channels
2.4 GHz 11g (draft)
5 GHz 11a
2.4 GHz 11b
Source: Agere, Atheros

## Slide 12: No Interferers means Ease of Use
2.4 GHz band is congested and interferers can affect setup and operation of networks
  Conflicting wireless networks
  Fixed wireless broadband
  Cordless phones
  Microwave ovens
  Security Systems
  Ham (Amateur) Radios
  Less than 100 MHz available (1 to 3 usable channels)
5 GHz band is clean spectrum operating under rules preventing narrowband interferers
  No conflicting protocols allow for true QoS and new applications
  Part 15 UNII spectrum rules prevent cordless phones, security systems, etc.
  Radiolocation satellites and Radars remote or in other parts of band
  Over 300 MHz available (4 to 19 usable channels)

## Slide 13: Myth of 2.4 GHz Range Advantage
5 GHz
2.4 GHz
Path Loss
+6dB

## Slide 14: Factors in WLAN System Range
5 GHz
2.4 GHz
Path Loss
+6dB
Equivalent
Antenna
Gain
+3dB
Tx
+3dB
Rx
Coding
Gain
Tx Power
Rx Sensitivity
Delay Spread
Tolerance

## Slide 15: Comparing 11a/b Measured Link Rates
Link rates of 802.11a are 2 to 5 times those of 802.11b at the same distance in actual tests
Data Link Rate (Mbps)
Range (ft)
~5x
~3x
Notes: This is optimal link rate – other rates could be supported…

## Slide 16: Still MANY Wireless Challenges Ahead
Networking ++
  Security (802.11i)
  Resource management, Scheduling, QoS (802.11e)
  Roaming, InterAccess Point Communications (802.11f)
Radio
  Range
  Efficiency in the use of spectrum
  Large range of “impairments” to be managed
  Managing interference (co-channel and adjacent channel)
  Regulatory (international acceptance) (802.11h)
Portability
  Battery life

## Slide 17: Security in Wireless LANS
There are three layers to wireless security, each relies on and complements the others
VPN, DRM
802.1x
WEP, TKIP, AES
Application
Authentication
Link Encryption

## Slide 18: Application Security
VPN’s provide end-to-end application security but creating a secure “tunnel” from the client to the server
VPN (Virtual Private Network)
Application
Advantage:
  Highest level of security from one end to the other
Disadvantage:
  Very complex and requires most effort to manage
  Affects performance, so hard to scale to large deployments

## Slide 19: Authentication
802.1x verifies that clients have the credentials to be on the network and increases the security of a data link
802.1x
Authentication
Advantage:
  Makes networks easier to manage by using extensible authentication methods to regulate access to a network
  Increases the security of a data link by refreshing WLAN encryption keys
Disadvantage:
  Weakened by poor data link level encryption

## Slide 20: Link Encryption
Encryption keeps intruders from eavesdropping on a link, but are dependent on a secure key
WEP
Link
Encryption
WEP The original Wired Equivalent Privacy protocol can be cracked by collecting and analyzing a sufficient amount of data – it needs either a VPN or 802.1x rekeying to be made secure
TKIP Temporal Key Initialization Protocol is a modification of WEP to defend against known attacks
AES The Advanced Encryption System is the one designated by the US Govt to replace the 3DES system commonly used in financial and other secure systems
TKIP
AES
More Secure

## Slide 21: Modern 802.11a Products are Highly Integrated
Digital Chip: MAC, Baseband
Processor, ADCs, DACs,
Memory
RF Chip: Power amp, LNA, VCO, SAW filtration, Frequency conversion, Frequency synthesizers, Variable gain amp
Power
Regulation
EEPROM
RF Filter
32MHz Crystal

## Slide 22: Mobility without Cost
Closing the gap with wired
Wireless PCMCIA connections relative to wired (wired =1)
0
0.5
1
1.5
2
2.5
1995
1997
1999
2001
2003
Cost
Speed

## Slide 23: Some Conclusions …
Unlicensed spectra and CMOS technology will combine to allow ubiquitous, low-cost, IP based wireless access (WLAN)
802.11, and 802.11a in particular, will dominate this WLAN landscape
WLANs are exciting
  Global and exponentially growing
  Technical innovation is rapid, continuing (hard problems to solve)
  Societal impacts have but begun to be seen (rapid change)
Future: Conclusions

## Slide 24
July 25, 2001