## Slide 1
Central Texas Telephone Cooperative, Inc.
BEST PRACTICE: Planning and Executing
A Profitable Coverage Plan
Broadband Wireless World Forum
February 12-14, 2002
Presented By: Larry D. Pechacek, P.E.
Central Texas Telephone Cooperative, Inc.
Chief Technology Officer

## Slide 2: CTTC Introduction
» Founded in 1951 in Goldthwaite Texas
» Serves Approximately 3,302 Square Miles
» Consists of 17 Telephone Exchanges with DSL Deployed
in all Exchanges
» Provides Approximately 7,600 Access Lines
» Member of the Texas Lone Star Fiber Network
» Provides Unregulated Services Through Central Texas Communications
» Provides Distance Learning by Connecting 12 Rural Schools

## Slide 3: CTC Introduction
» Formed in 1993 to Provide Wireless TV Services Using MDS & MMDS
» Serves Approximately 4700 Square Miles
» Consists of 3 Super Cells with Analog Head Ends
» Provides Video Broadcast Services to Approximately 3,000 Subscribers
» Provides Long Distance to CTTC Customers
» Operates an ISP Business Since 1996
» Participated in the 1997/1998 LMDS Auction and Acquired
A & B Spectrum Blocks in 2 Basic Trade Areas
Covering 19 County Area Consisting of 212,000 pops

## Slide 4: CTTC and CTC Coverage Areas

## Slide 5: Legacy Narrow Band Network

## Slide 6: Fixed Wireless (LMDS) and ATM Network Overlay

## Slide 7: Motivations for Wireless Technologies
» CTTC Services a High Cost Area - Alternative to Bulldozing and
Rock Sawing
» Expand Service Area
» Enable New Revenue Streams
» Enable Enhanced Services to our Communities
• Broad Band Services
• Cost Effective Packet Based Enabling Technologies
• Enhanced Voice Services (VoIP)
» CTC - Cost Efficient Local Loop Enabling Facilities Based
Full Services Telecommunications

## Slide 8: MMDS/LMDS - Market Considerations
» 2-Way MMDS:
• Large Radius of Coverage Area Suitable for Sparsely Populated Area
• Packet Based System
• Data Speeds up to Approximately 3 Mbps (DOCSIS)
• Significantly Lower CPE Costs
• Generally Suitable Technology for Residential, SOHO, and Small
Business
» LMDS:
• Short Radius of Coverage Area Suitable for Densely Populated Area
• Both ATM and Packet Based Systems Available
• Data Speeds up to Approximately 100 Mbps
• Relatively Higher CPE Costs
• Generally Suitable Technology for Small Through Very Large
Business

## Slide 9: MMDS & LMDS - Getting Started
» Use Spectrum We’ve Secured Over the Years
» Identified Requirements and Issued a Detailed Request for Proposal
to Selected Vendors
» Leveraging Existing Assets
• Fiber Network Into Surrounding Areas
• Reputation of Mobile Wireless Affiliate
• Wireless TV Facilities
» Selected Vendors and Deployed Evaluation Systems
LMDS: Newbridge Networks/Alcatel
Ensemble Communications
MMDS: Wavecom Communications and Cisco
» Perform Preliminary Network RF Planning

## Slide 10: MMDS/LMDS - Network Considerations
» Transport via ATM Network Allowing:
• Multiple Services via ATM Switch
• Circuit Emulation Interface To TDM Network
• Security via ATM VPI/VCI
• Access Concentration via ATM Switch Services
• Direct Network QoS Control
» Co-location of MMDS and LMDS Systems Where Needed
» Off Load Data Traffic From End Office Switch
» Off Load VoIP to local End Office Switch - Existing Class 5 Circuit
Switches With Appreciable Service Life From Both Financial
and Services Perspective
» Integrate Wireless Systems with Existing Wireline Network

## Slide 11: MMDS/LMDS - RF Planning Considerations
» MMDS/LMDS Sectorization Used to Accommodate Capacity
Requirements Characterized by Customer Density and Usage
Characteristics (Capacity and Symmetry)
» MMDS Will Begin with 3 Super Cells and Additional Mini/Micro Cells
on as Needed Basis As Dictated By Line-of-Sight Issues
» MMDS Requires Planning and Coordination with Surrounding BTA
Service Providers
» MMDS Radius of Coverage, Channel Bandwidth, and Modulation
Implementations Must be Coordinated for Best Fit to Requirements
» LMDS Requires Careful Radius of Coverage Determination Based Upon
Rain Fade and Reliability
» Permitting of Telecommunications Facilities Can be Problematic
» Frequency Planning for TDD Systems vs FDD Systems
» Land Base and RF Planning Software for Link Evaluation & Planning

## Slide 12: LMDS – Initial San Angelo, Tx RF Coverage

## Slide 13: LMDS - Project/Network Today
» Started With a 3 Base Station Deployment In San Angelo and a
one Base Station Deployment In Goldthwaite Using
Newbridge Networks Equipment
» Redeployed Using Ensemble Communications Equipment
» Currently Have:
• 4 Base Stations Deployed in San Angelo, with
15 Sectors Using both A and B Band Spectrum
• Approximately 52 Customers and 45 CPE Deployments
• Data and Voice (Limited) Services Provided and Looking
towards Video Services in the Future
Summary: Allowed us to go into San Angelo, a town of 100,000 people,
and very efficiently deploy facilities without overbuilding, and expand
our service area and create additional revenue streams as a full services
CLEC offering advanced broad band services.

## Slide 14: MMDS - Project/Network Today
» Have Deployed Evaluation System in Goldthwaite and Undergoing
Evaluation Testing
Summary: If it works as anticipated, and as we expect, the MMDS
wireless local loop will allow us to deliver broad band services cost
efficiently across our Cooperative area and potentially save us millions of
dollars. It will also allow us to cost efficiently expand our competitive
coverage areas into the surrounding rural areas.
» Have Deployed 8 Test CPE with Services Being Provided Up To 25 Miles
» Have Test Customer Installations Providing 2-Way Data and Analog
TV Using the Same Antenna. (Replace the receiver with a
transceiver and add a data modem)
» Using MDS I for Upstream and MMDS E1 for Downstream

## Slide 15: LMDS - WLL Characteristics
» Capable of Providing up to 3 and 5 Mile Coverage Radius
» Generally Proprietary Equipment Based Upon ATM and DOCSIS
Standards
» Data Delivery Speeds Developing Towards 100 Mbps
» RF Propagation is Line of Sight Limited
» RF Propagation Not Generally Subject to Multipath Interference
» Equipment Costs are Relatively Greater Compared to MMDS
» Cell (TDM via Circuit Emulation) and Packet Based Network Technology

## Slide 16: MMDS - WLL Characteristics
» Capable of Providing 25 to 30 Mile Coverage Radius
» Both Standards Based and Proprietary Solutions Available
» Data Delivery Speeds Up To 3 Mbps on Standards Based (DOCSIS)
» RF Propagation Relatively Unaffected by Rain
» RF Propagation is Line of Sight Limited (or Near Line of Sight)
» RF Propagation Subject to Multipath Interference (or Challenged)
» Equipment Costs are Relatively Lower Compared to LMDS
» Packet Based Network Technology

## Slide 17: MMDS/LMDS - Experiences To Date
» Experience Gained From Wireless TV Start-Up and Operations Have
Reduced Learning Curve for the 2-Way WLL Technology
and Start-up Issues/Concerns
» Experience Gained During First LMDS Deployment Has Been Very
Beneficial to Ascertaining Technology and Customer
Expectations
» Interconnection Agreement Negotiations Were Initially Tedious and
Lengthy; Today Favorable Agreements Exist That May be
Opted Into
» Zoning and Permitting of Telecommunications Facilities Can Be
Problematic
» Expect the MMDS and LMDS WLL Technologies Will Play a
Significant Role in Enabling Advanced and Broad Band
Telecommunications, and Expanding Our Service Area and
Revenue Options in a Cost Effective Manner

## Slide 18: MMDS/LMDS - Conclusion
» CTTC and CTC - Very Excited About the Economic and Service
Possibilities the MMDS and LMDS WLL Technologies Will
Enable for our Organizations in the Future
» We Believe WLL Technologies Will be an Important Asset Significant
to Surviving Forthcoming Regulatory Requirements and in an
Increasingly Competitive Environment
» We Believe WLL Technologies Will Potentially Save us Millions of
Dollars by Alleviating the Need to Rock Saw for Placing
Cable in the Ground
» We Believe WLL Technologies Will Prove to be a Cost Efficient
and Technically Capable Broadband Alternative.